## Slide 1
Graphs Tested:
Implemented Algorithm
Step 1: Read neighbours of 1st edge from table (memory) and store it locally.
Step 2: Check each neighbour for having a colour assigned to it. Assign
the lowest colour number not found in any neighbour to current edge. If new colour number was assigned, increase the required graph colours by 1.
Step 3: Having saved each neighbour from step 2, select the first neighbour saved to read as next memory and repeat step 2 until all neighbours from 1st edge are checked. If all neighbours are checked, read the second edge not already checked from memory (if only one is available, read that one). Repeat steps 2 and 3 until all edges have a colour assigned.
High Level Synthesis Lab
Task E
Check for coloured neighbours
Pick a colour based on neighbours found with colour
+1 for colours needed if new colour picked
Add not-coloured neighbours as next rows
Select next neighbour to read
If none select next row available to proceed.

## Slide 2
Pipelined whole module with II=2
Throughput = 11
High Level Synthesis Lab
Task E
Pipelined main ‘for’
loop only with II=1
Throughput = 12
Needs 1 more cycle
per graph but has a
‘safer’ slack.